## Slide 1: Oscillators and the Web Audio API
Josh Reiss
Professor of Audio Engineering
Queen Mary University of London
Blog: intelligentsoundengineering.wordpress.com/
Twitter: @IntelSoundEng
Youtube: www.youtube.com/user/IntelligentSoundEng
Publications: www.eecs.qmul.ac.uk/~josh/publications.htm

## Slide 2: Oscillators
Any periodic signal is an oscillator
Additive synthesis - Any signal can be created by summing up lots of simple oscillators
Standard oscillators include
  sine wave
  triangle wave
  square wave
  sawtooth wave
Created with the Oscillator Node
  Also allows you to create your own types of oscillators

## Slide 3: Sine wave
The basic building block of signals
Chart: 
  x(t)=sin()
  For =2

## Slide 4: Square wave
The basic building block of signals

## Slide 5: Triangle wave
The basic building block of signals

## Slide 6: Sawtooth wave
The basic building block of signals

## Slide 7: The Oscillator Node
Usage
or
Parameters
  type: Waveform shape; "sine" (default), "square", "sawtooth", "triangle“ or "custom"
  frequency: Frequency (in Hertz) of the periodic waveform. Default value is 440
  Detune: Offset the frequency by an amount (in cents) . Default is 0. So frequency becomes;
  computedOscFrequency = frequency2detune / 1200
var Tone = new OscillatorNode(context,{type:'sine',frequency:'440'})
Tone.start()
var Tone = context.createOscillator()
Tone.type = 'sine'
Tone.frequency.value = 440
Tone.start()

## Slide 8: How do you create your own custom oscillator type?

## Slide 9: Fourier series
Any periodic function x(t) can be represented by a Fourier series
Where f0 is the fundamental frequency of the periodic function
Or in complex form,
So the ans are known as the real terms, the bns as the imaginary terms.

## Slide 10: Example: Sine wave
All other terms are zero.
Chart: 
  x(t)=sin()
  For =2

## Slide 11: Example: Square wave
All other terms are zero.
Chart: 
First 3 terms.

## Slide 12: Example: Triangle wave
All other terms are zero.
First 3 terms.
Chart: Triangle Series

## Slide 13: Example: Sawtooth wave
Chart: Sawtooth Series
All other terms are zero.
First 3 terms.

## Slide 14: How many terms do you need in the Fourier Series?

## Slide 15: Aliasing
Two sinusoids, with frequency 3 Hz and 7 Hz
They appear identical when sampled at a frequency 10 Hz
Chart: 
10 Hz sampling | 1 | -0.30902 | -0.80902 | 0.80902 | 0.30902 | -1 | 0.30902 | 0.80902 | -0.80902 | -0.30902 | 1
Aliasing
  When signals become indistinguishable due to sampling
Shannon-Nyquist sampling theorem
  You need to sample at least twice every period
  in other words
  Sampling frequency should be at least twice the highest frequency in the signal
  Highest frequency in the signal should be less than half the sampling frequency
    Nyquist frequency= fs/2

## Slide 16: How many terms do you need in the Fourier Series?
Don’t keep terms beyond Nyquist
Example: Approximate a 4 kHz sawtooth wave with sampling frequency 44.1 kHz
Only keep terms below 22.05 kHz: 4,8,12,16 and 20 kHz
Recall Fourier series for sawtooth
Where f0=4000

## Slide 17: PeriodicWave
The Web Audio API allows you to create your own oscillator type with createPeriodicWave() and setPeriodicWave()
Create arrays of a values and b values for Fourier Series
Create the periodic wave by calling the audio context’s createPeriodicWave with a[] and b[]
Call the oscillator node’s setPeriodicWave with the periodic wave you just created
let source= context.createOscillator();
let a = new Float32Array(2);
let b = new Float32Array(2);
b[1]=1;
let myWave = context.createPeriodicWave(a,b);
source.setPeriodicWave(myWave);

## Slide 18: Pulse wave example
Square wave is a special case of a pulse wave
Pulse wave has an additional parameter,
  duty cycle = percentage of its period spent at its maximum value
  Square wave has duty cycle of 50%.
Consider pulse wave with a few more differences from the square wave
  Flips back and forth between 1 and 0, not +1 and -1
  Period T, duty cycle D/T
  At its maximum from time -D/2 to +D/2.
We can write one period as;
Chart: Pulse Wave
Pulse wave, 75% duty cycle, 2 Hz frequency

## Slide 19: Pulse wave example
Chart: Pulse Wave
Coefficients are known to be
<button onclick="context.resume()">Start</button>
<p>Frequency</p>
<input type="range" min=1 max=1000 value=10 id="Frequency">
<p>Duty Cycle</p>
<input type="range" max=1 step='any' value=0.5 id="DutyCycle">
<script>
let context= new AudioContext();
let source= new OscillatorNode(context,{frequency:10});
var maxCoef= context.sampleRate/(2*source.frequency.value);
var a = new Float32Array(context.sampleRate/2);
var b = new Float32Array(context.sampleRate/2);
real[0]=0,imag[0]=0;
for (i=1;i<maxCoef;i++) a[i]= 2*Math.sin(i*Math.PI*DutyCycle.value)/(i*Math.PI);
source.setPeriodicWave(context.createPeriodicWave(a,b));
source.connect(context.destination);
source.start();
Frequency.oninput = function() { source.frequency.value = this.value }
DutyCycle.oninput = function() {
maxCoef= context.sampleRate/(2*source.frequency.value);
for (i=1;i<maxCoef;i++) real[i]= 2*Math.sin(i*Math.PI*DutyCycle.value)/(i*Math.PI);
source.setPeriodicWave(context.createPeriodicWave(real,imag));
}
</script>
Why is there an offset?
Recalculate the coefficients, up to Nyquist, for this new Duty Cycle
Set the coefficients of the Fourier series
Create and set the periodic wave on one line
Only keep terms in Fourier series below Nyquist