## Slide 1
Filters
And filtering in the Web Audio API

## Slide 2: Simple digital filter
Linear time invariant digital filters are at the heart of many audio effects
Current output y[n] is a function of summed and weighted values of
  Current input x[n]
  Past input x[n-1], x[n-2], …
  Past output y[n-1], y[n-2], …
Difference equation:
a0 y[n] + a1y[n -1] + …+ aNy[n-N] =b0x[n] + b1x[n-1] +…+ bMx[n-M]
Examples:
  Simple delay: y[n] = x[n-D]
  Averaging: y[n] = 0.5x[n] + 0.5x[n-1]
  Exponential smoothing: y[n] = cx[n] + (1-c)y[n-1]

## Slide 3: Simple digital filter
Filter can be completely described by coefficients
  a1, ..., aN, b0, b1, ..., bM
Filters affect the magnitude and phase of frequencies in a signal
  Input: x[n]=sin(n)
  Apply filter: y[n]= 0.5x[n] + 0.5x[n-1]
  y[n]= (sin(n) + sin(n-1))/2
  = cos(1/2) sin(n-1/2)
Phase change
Magnitude change

## Slide 4: Ideal filters
Y-axis: Output magnitude
X-axis: Input frequency
Fc: cut-off or centre frequency
B: bandwidth
0
Fs/2
1
fc
0
Fs/2
fc
1
0
Fs/2
fc
1
0
Fs/2
fc
1
B
B
Lowpass
Highpass
Bandpass
Notch
0
Fs
1
fc
G
0
Fs
fc
1
G
0
Fs
fc
1
G
0
Fs
fc
1
G
Peaking Filter
Allpass Filter
Low Shelving Filter
High Shelving Filter

## Slide 5: Ideal filters
0
Fs
1
fc
G
0
Fs
fc
1
G
0
Fs
fc
1
G
0
Fs
fc
1
G
Peaking Filter
Notch Filter
Low Shelving Filter
High Shelving Filter
Y-axis: Output magnitude
X-axis: Input frequency
Fc: cut-off or centre frequency
B: bandwidth
G: gain

## Slide 6: Types of filters
Lowpass
Highpass
Bandpass
Peaking / Notch
Shelving
Allpass
Types we frequently encounter in audio systems:

## Slide 7: Filter Q
Filters can often be described by “quality factor” Q
  Selectivity (bandwidth) relative to centre frequency
Q=Centre frequency / bandwidth = fc/B
Q = 0.5
Q = 0.71
Q = 1
Q = 1.5
Q = 3
Q = 10
Second order
lowpass resonator filters

## Slide 8: Filtering in the Web Audio API
Two types of audio nodes for filtering
BiquadFilterNode
  2nd order: a0 y[n] + a1y[n -1] + a2y[n-2] = b0x[n] + b1x[n-1] + b2x[n-2]
  Parameters specify the filter type and attributes
IIRFilterNode
  IIR stands for infinite impulse response
    feedback from a1, a2, … so it responds forever to a pulse input
    to finite impulse response where output depends only on current and previous inputs
  Arbitrary order
  Parameters specify the filter coefficients
   Once the node has been created, you can't change its coefficients

## Slide 9: BiquadFilter types and parameters
Type | Description | Frequency | Gain | Q
lowpass | Resonant lowpass filter. Attenuates frequencies above cutoff. | Cutoff frequency | - | Large value makes response more peaked at cutoff
highpass | Opposite of lowpass | Cutoff frequency | - | Large value makes response more peaked at cutoff
bandpass | Passes only frequency band | Center frequency | - | Less bandwidth for high Q
lowshelf | Boosts or cuts lower frequencies | Cutoff frequency | Boost or cut in dB | -
highshelf | Opposite of lowshelf | Cutoff frequency | Boost or cut in dB | -
peaking | Boost or cut frequency band | Center frequency | Boost or cut in dB | Less bandwidth for high Q
notch | Opposite of bandpass | Center frequency | - | Less bandwidth for high Q
allpass | Changes phase relationship between various frequencies | Frequency where phase transition occurs | - | How sharp phase transition is