## Slide 1
Convolution and Reverb in the Web Audio API

## Slide 2: What is reverberation?
Series of delayed and attenuated sound waves
  Result of many reflections within a space
Multiple paths from a source to our ears
  Direct path
    Strongest and first
  Reflected paths, bouncing off walls or ceiling
    Weaker and arrive later
Creates spaciousness of a room
Source
Microphone

## Slide 3: Impulse response
Series of scaled delta functions
Each vertical line marks when sound heard again
  represents delayed, attenuated copy of sound
Height of lines represents how loud sound is at that time
What would simple feedback delay look like?
Early
Reflections
Late
Reflections
Time
Magnitude

## Slide 4: Why use reverb?
Why add artificial reverb to recorded sound?
  Dry signals (e.g. close mic) sound unnatural
  Compensate for non-reverberant listening environment
    Headphones have no natural reverb
    Car or small room might not have sufficient reverberance to recreate sound of orchestra in concert hall
Can add natural reverb by recording in large room
  Distant microphones capture ambience as well as direct signal
  Impractical in many situations
   Add reverb synthetically

## Slide 5: Convolution Reverb
Reverb can be completely characterised by its impulse response
Suppose we have impulse response of a room
  Record impulse (like popping balloon) with microphone in one location, sound source in another location
Apply reverb by convolving signal with recorded impulse response
  Makes it sound as if it is in the space

## Slide 6: ConvolverNode
Convolution
ConvolverNode performs convolution on an AudioBuffer
Used to achieve a reverb effect
Always has exactly one input and one output
Properties
    buffer - mono, stereo, or 4-channel AudioBuffer containing (possibly multichannel) impulse response used by ConvolverNode
    normalize - boolean that controls whether impulse response will be scaled by an equal-power normalization. Default is true
Lets demonstrate convolution for short pulse convolved with simple one channel buffer

## Slide 7: Setting up an audio buffer
AudioBuffer represents short audio asset in memory
  typically less than 45 s
  created from audio file using AudioContext.decodeAudioData() method, or from raw data using AudioContext.createBuffer().
Once put in an AudioBuffer, audio can be played by being passed into an AudioBufferSourceNode
  For longer sounds, MediaElementAudioSourceNode is more suitable
Buffer contains data as arrays with values between -1 and +1
Lets create an impulse response (IR)
Here, decay >0 is the rate of decay
Impulse response can also come from a recording
function impulseResponse(duration,decay) {
var length = context.sampleRate * duration;
var impulse = context.createBuffer(1,length,context.sampleRate);
var IR = impulse.getChannelData(0);
for (var i=0;i<length;i++) IR[i] = (2*Math.random()-1)*Math.pow(1-i/length,decay);
return impulse;
}

## Slide 8: Applying convolutional reverb
Lets create short sinusoidal pulse of 100 ms as our source
  Connect an oscillator to a gain
  Have the gain node’s gain parameter jump to 0 after 0.1 s
Create impulse response using function shown previously
Set that as the buffer of the convolver
Simply connect the pulse to the convolver
Compare this with the pulse without reverb
  Connect amplitude (instead of convolver) to destination
var context = new AudioContext();
var source = new OscillatorNode(context,{type:’sine'});
source.start();
var amplitude = new GainNode(context);
amplitude.gain.setValueAtTime(0,context.currentTime+0.1);//pulse lasts 100 ms
var impulse=impulseResponse(1,2);//1 second impulse, with decay value 2
var convolver = new ConvolverNode(context,{buffer:impulse});
source.connect(amplitude);
amplitude.connect(convolver);
convolver.connect(context.destination );

## Slide 9
Buffer[0]
Buffer[0]
Buffer[1]
Mono with mono response
  ‘mono’
Mono with stereo response
  ‘mono to stereo’
Mono with stereo matrix response
Buffer[0]
Buffer[1]
Buffer[2]
Buffer[3]
Stereo with mono response
Stereo with ‘true’ stereo matrix response
  ‘true stereo’
Stereo with stereo matrix response
  ‘normal stereo’
Buffer[0]
Buffer[1]
Buffer[2]
Buffer[3]
Buffer[0]
Buffer[1]
Buffer[0]
Buffer[1]
Notes: single channel convolution operates on a mono audio input, using a mono impulse response, and generating a mono output. 1->1
Then mono to stereo 1-2
Stereo to mono 2->1
The remaining images illustrate the cases for mono and stereo playback where the number of input channels is 1 or 2, and the number of channels in the buffer is 1, 2, or 4. If you want other matrixing options, you can use the ChannelSplitterNode, multiple single-channel ConvolverNodes and then a ChannelMergerNode.

## Slide 10: One block convolution
N N
h zeros
SkN:(k+1)N-1 zeros
FFT
FFT
X
IFFT
r
2N

## Slide 11: One block convolution
N N
h zeros
Input buffer zeros
FFT
FFT
X
Output spectral frame
2N
Input spectral frame
Complex multiply
IFFT
Output frame Save 2nd half
Convolution kernel

## Slide 12: Partitioned convolution for real-time artificial reverberation
r
h
s0:N-1*h
h
h
h
s0:N-1
sN:2N-1
s2N:3N-1
s3N:4N-1
sN:2N-1*h
s2N:3N-1*h
s3N:4N-1*h
…
…
…
…
…
…
…
Sum end of previous convolution and beginning of current convolution
{
Convolve impulse response and the current block
{
s

## Slide 13
Buffer[0]
Buffer[1]
Buffer[2]
Buffer[3]
Buffer[0]
Buffer[1]
Buffer[0]
Buffer[1]
Notes: single channel convolution operates on a mono audio input, using a mono impulse response, and generating a mono output.
The remaining images illustrate the cases for mono and stereo playback where the number of input channels is 1 or 2, and the number of channels in the buffer is 1, 2, or 4. If you want other matrixing options, you can use the ChannelSplitterNode, multiple single-channel ConvolverNodes and then a ChannelMergerNode.
2->4
1->4

## Slide 14
Source
Microphone